## Slide 1
Interrupts in Embedded
Systems

## Slide 2
Polling
The microcontroller constantly checks for the state of an input pin inside a loop without continuing any other operation.
When the state of the pin satisfies the condition, the corresponding task is performed.
while(1)
{
if(condition)
{
//task
}
}
The disavantage is that no other task can be done while the MCU is cheking for the status of input pin.

## Slide 3
What is an Interrupt?
It is something that allows you to interrupt the current running code in order to perform another action, and once done resume the function that it interrupted.
But why do we need it?
Micro controllers interact with the physical world. The physical world is unpredictable, events happen at random intervals and sometimes they have to be dealt with right away to prevent hardware damage or data loss.

## Slide 5
Now we have 2 questions for you!!
If two different commands are to be executed when two different conditions are met how will you write the commands?
If two or more interrupt requests are triggered at the sametime which one will get executed first?
Notes: 5

## Slide 6
This image holds the answer for both these questions!
Interrupt vector table

## Slide 7
We use the specific ‘vector’ name for the interrupt to specify the commands to be executed during the respective interrupt request
If two or more requests are triggered at the same time the order given in the table is followed.
Ex: If suppose INT0,INT1 and reset are triggered,this order is followed,
Reset
INT0
INT1

## Slide 8
Syntax for interrupt definition
Example:

## Slide 9
External interrupt in Atmega 328
The two shown pins PD2(INT0) or PD3(INT1) can be used to trigger the external interrupt

## Slide 10
Enabling and disabling interrupts
Firstly, globally enable all interrupts
This is done by setting I bit of SREG register.
Setting it up high can be done by in-built function
sei();
Similarly , clearing it is done by cli();

## Slide 11
External interrupts
One of the important types of interrupts is the external interrupt
It is one of the important ways where we can control the functioning of the microcontroller externally.
It can be triggered using a tactile switch(push button), IR modules etc.
Tact switch (push button)
IR module

## Slide 12
How to go about enabling external interrupt
1)Globally enable interrupts by sei();//As discussed before.
2) #### A very important note#####
When using external interrupt, the above pins should be in input mode.
EICR

## Slide 13
3) Specify whether interrupt signal should be generated on rising or falling edge or either of them or even low level triggered by giving appropriate values to ISCxx bits of EICRA(External Interrupt Control Register A).
4) Finish by completing the ISR with appropriate vector name

## Slide 14
Flag register for External interrupts
Each interrupt has a corresponding flag register
When the event specified by the Interrupt Sense Control (ISCxy) bits in the MCU Control Register (MCUCR) is sensed on the INTx pin, the External Interrupt Flag x (INTFx) in the External Interrupt Flag Register (EIFR) is set HIGH (1).
If the I-bit in SREG and the INT1 bit aree both HIGH(1) the MCU will jump to the corresponding vector. The Flag is set to LOW (0) when the INTx_vect routine is executed.