## Slide 1: GENESIS ‘17

## Slide 2: BASICS OF ELECTRONICS

## Slide 3: RESISTORS
What is this resistor used for?
passive two-terminal electrical component

## Slide 4: RESISTORS
So how do we find the value of this resistance?
Used to limit current in a circuit to protect components such as LEDs
Used as a voltage divider.

## Slide 5: RESISTORS COLOR CODE FOR CARBON RESISTORS

## Slide 6: PHOTORESISTOR
Value of resistance changes with the light incident on it
So how does this happen?

## Slide 7: PHOTORESISTOR
made of semiconductor material
When light falls on photoresistor , some of the electrons jump from valence to conduction band and conduct current.
When light energy increases , more number of free electrons are generated and hence resistance is less.

## Slide 8: CAPACITOR
A device used to store an electric charge, consisting of one or more pairs of conductors separated by an insulator.

## Slide 9: POTENTIOMETER
Can be used as a voltage divider or as a variable resistor(rheostat)

## Slide 10: POTENTIOMETER
The resistance can be varied by placing the wiper anywhere between the terminals A and B.
It can be used as an ‘adjustable voltage divider’ by using all 3 terminals.

## Slide 11
Current
Voltage
Resistance
Continuity
Multimeter basics

## Slide 12: CHECKING CONTINUITY

## Slide 13: MEASURING CURRENT

## Slide 14: MEASURING POTENTIAL DIFFERENCE
DC
AC
MEASURING RESISTANCE
DO NOT CONNECT PROBES DIRECTLY TO HOUSEHOLD AC MAINS!!!
PRECAUTION

## Slide 15: VOLTAGE REGULATORS(78XX SERIES)
Made of zener diodes and transistors
It basically gives a fixed output for a wide range of inputs.
Eg:
7805 gives a 5V as output as long as the input voltage is between 7V and 35V

## Slide 16: OPERATIONAL AMPLIFIER COMPARATOR(Op-Amps)
ANALOG SIGNAL
DIGITAL SIGNAL
It can have any value between the peak voltages at any instant of time.
It can have only finite number of values at different instants.
It takes only discrete values
Here it takes only 2 values 0(Low) and 5v(High).

## Slide 17: OPERATIONAL AMPLIFIER COMPARATOR(Op-Amps)
It compares the input voltage and fixed reference voltage and produces output accordingly.

## Slide 18: OPERATIONAL AMPLIFIER COMPARATOR(Op-Amps)
If V+ > V then Vo=Vcc
(Digital High 1 output)
If V+ < V then Vo=0
(Digital Low 0 output)

## Slide 19: OPERATIONAL AMPLIFIER COMPARATOR(Op-Amps) INTERNAL CIRCUITRY

## Slide 20: OPERATIONAL AMPLIFIER COMPARATOR(Op-Amps)
LM358- Dual Comparator

## Slide 21
So till now we saw so many components. But how do I make a circuit out of them or connect them together and test circuits???

## Slide 22: BREADBOARD

## Slide 23: BREADBOARD-CONNECTIONS
The black line shows the columns and rows which are connected.
Now try connecting 2 resistors
in series and then in parallel

## Slide 24
Parallel:
Series:
Notes: MODULE

## Slide 25: DIODES
Conducts primarily in one direction
Similar to flow of water in a valve
Zener diode
LED
Photo diode

## Slide 26: LIGHT EMITTING DIODE(LED)
The colour of the light emitted depends on the band gap energy of the diode.
Longer leg is anode, shorter leg is cathode

## Slide 27: LIGHT EMITTING DIODE(LED)
WARNING!!!
Never connect an LED directly without a resistor

## Slide 28: INFRARED LED
It emits in the infrared region and not in the visible range

## Slide 29: ZENER DIODE
It operates mainly in reverse bias.
It is used as a voltage regulator.

## Slide 30: PHOTODIODE
Connected in reverse bias
Converts light into an electrical current.

## Slide 31: Let’s Try This Out!!
Make a black and white color sensor. Your circuit must respond (say Turn ON or OFF an LED) depending on the color that you show to your circuit. (You do not need any thing more than an Opto-coupler pair , an LED and a comparator to do this!!)

## Slide 32
IR LED SENSOR